## Slide 1
Prototyping
Firebox-0
Nathan Pemberton Joao Carreira Zach Rowinski Martin Maas
+ The Entire Firebox Group
Krste Asanović Randy Katz

## Slide 2
FireBox-0
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 3
What is Firebox – 0?
- Firebox – 0 Cluster:
16-node cluster
1 Infiniband switch
1 Ethernet switch
- Node configuration:
Intel Ivy Bridge 8Cores / 16Threads 3.0GHz 25MB
64GB RAM (1TB aggregate)
2 Samsung SSDs (120GB + 480GB) (9.4TB aggregate)
Infiniband: Mellanox ConnectX-3 VPI FDR QSFP 56Gbps
Ethernet: Mellanox ConnextX-3 EN QSFP 40Gb
Running Ubuntu 14.04 (Linux 3.13.0)
Notes: Brief overview of Hardware / Software configuration of Firebox
Aggregate memory and disk capacity:
- 1TB of RAM
- ~9.4TB of SSD storage

## Slide 4
FireBox Software Stack
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager (Mesos + interactive)
Batch
New component
Modified existing component
Unmodified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 5
Tessellation
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager (Mesos + interactive)
Batch
New component
Modified existing component
Unmodified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 6: Tessellation
Adaptive Resource Centric Computing (ARCC)
  Package applications into cells with explicit resource allocation and QoS guarantees
  Manage cells and resource allocation through a thin control plane
Service-oriented
  Cells subscribe to services provided by other cells
  Service subscriptions == resource allocations
Application1
QoS-aware
Scheduler
GUI
Service
Running System
(Data Plane)
Performance
Reports
Resource
Assignments
Control
Plane
Cell
Application1
Cell
QoS-aware
Scheduler
Block
Service
QoS-aware
Scheduler
NW
Service
Channels

## Slide 7: Implementation
Observation: If the Tessellation kernel looks like a hypervisor, why not just use a hypervisor?
Tessellation implements these concepts on top of Xen
  Xen Domains become Cells
  Pluggable Schedulers allow us to implement custom scheduling policies
  Build network or other services in stub-domains (Xen domains intended to run drivers)
  Run Linux or a custom Library OS in the cells instead of mandating a particular interface

## Slide 8: Tessellation
Physical Node
Tessellation OS (modified Xen)
Cell Scheduler
RAB
Service
Resource Monitor
Traditional Cell
Linux
Cluster Manager
Exec Framework
User App
Tess Cell
LibOS
User App
Unified Inter-node
and Intra-node IPC
interfaces
Most cells run modified
OS and applications to take
full advantage of Tessellation
features
Traditional virtual-machine
approaches continue to work
Tess kernel
Provides QoS and ARCC mechanisms
Resource allocation broker provides QoS and ARCC policy
Cell Communication Channels

## Slide 9: Tessellation: Status
Scheduling
  Implemented gang scheduler to enable more effective 2-level scheduling
  Results show potential for some workloads but reduced CPU utilization for others
  Needs more experimentation with complex user-level frameworks
CellOS
  CellOS is a stripped down OS Based on Guk1 and newLib2
    Supports a subset of POSIX
  Pthread based benchmarks have been ported (e.g. CoEVP and CoHMM)
  Experiences
    Some single-application benchmarks are slower on CellOS than on Linux
    Debugging is very difficult
    More work is needed to improve performance and usability

## Slide 10
Firebox-0 Benchmarks
“WSC Executive”
Bulk Memory API
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager
Batch
Network
Set of benchmarks across the Firebox-0 stack:
Network (RDMA latency / bandwidth)
Key-value stores (RAMCloud, Aerospike Cassandra)
Interactive (Apache Solr)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 11
Firebox-0 Network
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager (Mesos + interactive)
Batch
New component
Modified existing component
Unmodified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 12
Firebox-0 Network Latency / Bandwidth
RDMA Ping Pong Benchmark:
  RDMA connection is setup through
  TCP/IP
  Sequential RDMA reads with different
  sizes
Latency:
  Latency of 1.7us for small packets
  High latency for big (>1MB) packets
  Bandwidth:
  Low bandwidth for small packets
  Maximum bandwidth of ~5 GB/s
Notes: Raw benchmark of Firebox Network
TODO:

## Slide 13
Key-value stores on Firebox-0
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager (Mesos + interactive)
Batch
New component
Modified existing component
Unmodified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 14
Benchmark of Key-value stores
Key-value stores benchmarked:
RAMCloud (RAM storage system with low-latency RPCs)
Aerospike (flash-optimized key-value store)
Cassandra (semi-structured and scalable key-value store)
Name | Atomicity / Consistency | Durability / Replication | Latency
RAMCloud | Atomic single-key updates. Supports conditional updates | Data is replicated to other nodes (RAM) and written to disk asynchronously | Ultra-low
Aerospike | Atomic single-key update. Supports atomic multi-key reads | Data is replicated and written to disk sync/asynchronously | Low
Cassandra | Tunable / linearizable consistency No atomic writes across replicas | Data is replicated and written to disk sync/asynchronously | Low -Medium
Notes: Key-value stores.
1) What is RAMCloud?
DRAM-based storage system
The case for RAMCloud
http://delivery.acm.org/10.1145/1970000/1965751/p121-ousterhout.pdf?ip=2.83.55.65&id=1965751&acc=OPEN&key=4D4702B0C3E38B35%2E4D4702B0C3E38B35%2E528120C21059793D%2E6D218144511F3437&CFID=551422919&CFTOKEN=31387118&__acm__=1420299996_3806cb8ae5b1fc2b0b8d8d4351f9242b
http://web.stanford.edu/~ouster/cgi-bin/papers/ramcloud-recovery.pdf

## Slide 15
RAMCloud
Latency / Bandwidth:
67-107% higher read bandwidth
45-53% lower read latency
Challenges:
ACID multi-key transactions with
low-latency and at scale
ClusterPerf:
RAMCloud test suite (eg., multiReads)
We use one test (sequential read/write of
random objects)
RAMCloud:
4 nodes, replication factor = 0
Notes: Mention best hardware
Remove ‘basic’

## Slide 16
AeroSpike + Cassandra (YCSB)
YCSB:
32 concurrent clients
6 workloads
Aerospike and Cassandra setup:
4 nodes
Replication factor = 3
YCSB results:
Sub-millisecond average read latency for
both Aerospike and Cassandra
Aerospike with higher throughput for workload
D (read latest) and E (short ranges)
Notes: Two key-value stores:
Aerospike:
In-memory NoSQL key-value store. Optimized for flash storage. Can achieve high throughput
Cassandra:
How does YCSB work:
1)
2)
3)
- YCSB
Workloads:
A:
B:
C:
D:
E:
F:

## Slide 17
Interactive Applications on Firebox-0
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Batch
Interactive
Hadoop
Spark
App
App
Cluster Manager (Mesos + interactive)
Batch
New component
Modified existing component
Unmodified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 18: Benchmarking Distributed Search: Apache Solr on Firebox-0
Goal: Test latency sensitive (interactive) applications on Firebox-0
Apache Solr is a popular open source program for text search with widespread use
Fan-out pattern -- many machines piece together the search response for a user
Distributed search architecture

## Slide 19: Solr on Firebox-0
Solr cluster: 1 Solr instance -> 1 core. Data sharded evenly amongst instances and stored locally.
Zookeeper for cluster management.
Hadoop and HDFS (optional)
Notes: This is what Solr looks like on Firebox now
Solr on Firebox has two major components, the server and client. The server consists of a cluster of solr instances spread across many machines, together with a separate set of machines hosting Zookeeper. Zookeeper is responsible for cluster management and synchronization amongst the Solr instances; it knows if and when a node goes offline and communicates that to the Solr instances so they can reroute traffic accordingly. Each solr instances locally maintains a part of the index (shard) as well as maybe replicas.

## Slide 20: Experiment: Latency and IO
Challenges benchmarking large distributed systems
many free parameters
exogeneous factors that disrupt performance can be hard to find and diagnose
Caching effects at the disk, OS, and program level have a significant impact on latency
Java GC is unpredictable
Samsung SATA vs. PCIe, 2 shards, no replicas, 50 million indexed documents, 4 GB heap max, default GC settings
PCI-Express ~25% lower latency
Notes: This experiment is designed less for low latency or high query rate than it was to take advantage of disk bandwidth. You can see the PCIe SSD interface is roughly 25 % in this experiment. In this case, the Solr index is large (~30 GB a shard). It can fit in memory but suffers from high GC activity that kill latency performance.
What happens if attempt to keep search index on disk, rather than load it into memory...

## Slide 21: Testing Framework (BITS)
Python scripts for
  Setup and takedown of application and data
  Visualizing results with Matplotlib
  Orchestrating tests & gathering data from tools
Make use of common performance monitoring tools
  Load generators: Iago, Jmeter.
  CPU & Memory: VisualVM, Sematext SPM, Ganglia
  Network: bwm-ng (coarse monitoring), IO: iotop
VisualVM: CPU and Memory monitoring

## Slide 22: Future Work
Tessellation
  Still early days: Most features yet to be implemented
  Big area of interest: 2-level scheduling and resource allocation
    Gang scheduling needs deeper analysis and more sophisticated implementation
    Advantages of minimal OS vs Linux
  Need to run Firebox benchmarks on Tessellation
Increase number of benchmarks
  A number of genomics and big-data style workloads are running on EC2, need to run on Firebox-0
  Other important workloads we are missing?
Understand Aerospike vs Cassandra results

## Slide 23: Questions

## Slide 24: Backup Slides

## Slide 25: Gang Scheduling Experiments
Micro-benchmark
  Run identical, compute-bound tasks on multiple threads repeatedly
  Record each time a thread completes its task more than a full iteration behind the others (a missed deadline)
Macro-Benchmarks
  HPC benchmark that models solid deformation in extreme environments
  Ran multiple instances of the benchmark
    Batch: Each instance ran one after the other
    Credit: Simultaneous execution on Xen’s default (non-gang) scheduler
    Gang: Simultaneous execution with gang scheduling

## Slide 26: Micro Benchmark Results

## Slide 27: Macro Benchmark Results

## Slide 28
Firebox Network
Without VMA* | 4.8 us
With VMA | 1.3 us
SockPerf Ping Pong Latency in Fbox
Firebox v0 | 1.7 us
RAMCloud HW [1] | 3.1 us
RDMA Ping Pong Latency
*VMA = Mellanox socket library with kernel bypass
Notes: Raw benchmark of Firebox Network
TODO:

## Slide 29
Aerospike/Cassandra Write Latency
Notes: Raw benchmark of Firebox Network
TODO: