## Slide 1
Prototyping
Firebox-0
Nathan Pemberton Joao Carreira Zach Rowinski
Martin Maas Frank Nothaft
Krste Asanović Randy Katz

## Slide 2
This Talk
Hardware
Resource Management
Frameworks and Runtimes
Applications and Services
Firebox Software Stack
Firebox software stack spans multiple layers: from Racks to Apps
Talk :
  Benchmarks of different layers of the stack
  Early project building a new Xen-based hypervisor (XARCC)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 3
What is Firebox – 0?
- Cluster:
16-node Infiniband-connected cluster
Fbox: externally-visible node
- Hardware configuration:
Intel Ivy Bridge 8Cores / 16Threads 3.0GHz 25MB
64GB RAM per node (1TB aggregate)
2 Samsung SATA SSDs per node (120GB + 480GB) (9.4TB aggregate)
2 extra Samsung PCIe SSDs (734GB)
Infiniband: Mellanox ConnectX-3 VPI FDR QSFP 56Gbps
Ethernet: Mellanox ConnextX-3 EN QSFP 40Gb
Running Ubuntu 14.04 (Linux 3.13.0)
Firebox-0 goal:
            Looking glass to 2014 off-the-shelf hardware and software
F1
….
Fbox
Ethernet (Mellanox)
Infiniband (Mellanox)
F16
Notes: Brief overview of Hardware / Software configuration of Firebox
Aggregate memory and disk capacity:
- 1TB of RAM
- ~9.4TB of SSD storage

## Slide 4
Firebox-0 Software Stack
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Interactive Applications
Cluster Manager (Mesos + interactive)
New component
Modified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 5
Firebox-0 Benchmarks
“WSC Executive”
Bulk Memory API
Interactive Applications
Cluster Manager
Network
Apache Solr
RAMCloud, Aerospike,
Cassandra
Set of benchmarks across the Firebox-0 stack:
RDMA
Latency / Bandwidth
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 6
Firebox-0 Network Latency / Bandwidth
RDMA Ping Pong Benchmark:
  RDMA connection is setup through
  TCP/IP
  Sequential RDMA reads with different
  sizes
Latency:
  Latency of 1.7us for small packets
  High latency for big (>1MB) packets
  Bandwidth:
  Low bandwidth for small packets
  Maximum bandwidth of ~5 GB/s
Notes: Raw benchmark of Firebox Network
TODO:

## Slide 7
Firebox-0 Key-value stores
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Interactive Applications
Cluster Manager (Mesos + interactive)
New component
Modified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 8
Benchmark of Key-value stores
Key-value stores benchmarked:
RAMCloud (RAM storage system with low-latency RPCs)
Aerospike (flash-optimized key-value store)
Cassandra (semi-structured and scalable key-value store)
Name | Atomicity / Consistency | Durability / Replication | Latency
RAMCloud | Atomic single-key updates. Supports conditional updates | Data is replicated to other nodes (RAM) and written to disk asynchronously | Ultra-low
Aerospike | Atomic single-key update. Supports atomic multi-key reads | Data is replicated and written to disk sync/asynchronously | Low
Cassandra | Tunable / linearizable consistency No atomic writes across replicas | Data is replicated and written to disk sync/asynchronously | Low -Medium
Notes: Key-value stores.
1) What is RAMCloud?
DRAM-based storage system
The case for RAMCloud
http://delivery.acm.org/10.1145/1970000/1965751/p121-ousterhout.pdf?ip=2.83.55.65&id=1965751&acc=OPEN&key=4D4702B0C3E38B35%2E4D4702B0C3E38B35%2E528120C21059793D%2E6D218144511F3437&CFID=551422919&CFTOKEN=31387118&__acm__=1420299996_3806cb8ae5b1fc2b0b8d8d4351f9242b
http://web.stanford.edu/~ouster/cgi-bin/papers/ramcloud-recovery.pdf

## Slide 9
RAMCloud
Latency / Bandwidth:
67-107% higher read bandwidth
45-53% lower read latency
Challenges:
ACID multi-key transactions with
low-latency and at scale
ClusterPerf:
RAMCloud test suite (eg., multiReads)
We use one test (sequential read / write of
random objects)
RAMCloud:
4 nodes, replication factor = 0
Notes: Mention best hardware
Remove ‘basic’

## Slide 10
AeroSpike + Cassandra (YCSB)
- YCSB:
32 concurrent clients from Firebox
- Aerospike and Cassandra setup:
4 nodes
Replication factor = 3
YCSB results:
Sub-millisecond average read latency for
both Aerospike and Cassandra
Aerospike with higher throughput for workload
D (“read latest”) and E (“short ranges”)
Notes: Two key-value stores:
Aerospike:
In-memory NoSQL key-value store. Optimized for flash storage. Can achieve high throughput
Cassandra:
How does YCSB work:
1)
2)
3)
- YCSB
Workloads:
A:
B:
C:
D:
E:
F:

## Slide 11
Interactive Applications on Firebox-0
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Interactive Applications
Cluster Manager (Mesos + interactive)
New component
Modified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 12: Benchmarking Distributed Search: Apache Solr on Firebox-0
Goal: Test latency sensitive (interactive) applications on Firebox-0
Apache Solr is a popular open source program for text search with widespread use
Fan-out pattern -- many machines piece together the search response for a user
Distributed search architecture

## Slide 13: Solr on Firebox-0
Notes: This is what Solr looks like on Firebox now
Solr cluster: 1 Solr instance -> 1 core. Data sharded evenly amongst instances and stored locally.
Zookeeper for cluster management.
Hadoop and HDFS (optional)
Solr on Firebox has two major components, the server and client. The server consists of a cluster of solr instances spread across many machines, together with a separate set of machines hosting Zookeeper. Zookeeper is responsible for cluster management and synchronization amongst the Solr instances; it knows if and when a node goes offline and communicates that to the Solr instances so they can reroute traffic accordingly. Each solr instances locally maintains a part of the index (shard) as well as maybe replicas.

## Slide 14: Experiment: Serving a large search index off of disk
Challenges benchmarking large distributed systems
Caching effects at the disk, OS, and program level have a significant impact on latency
Java GC is unpredictable - See Martin’s talk
many permutations of parameters to choose from for any given test
exogeneous factors that disrupt performance can be hard to find and diagnose
Samsung SATA vs. PCIe SSDs, 2 shards, no replicas, 50 million indexed documents, 4 GB heap max, default GC settings
PCI-Express ~25% lower latency
Latency (ms)
Test run
Test run
Search latency, average
Search latency, 99th percentile
Notes: This experiment is designed less for low latency or high query rate than it was to take advantage of disk bandwidth. You can see the PCIe SSD interface is roughly 25 % in this experiment. In this case, the Solr index is large (~30 GB a shard). It can fit in memory but suffers from high GC activity that kill latency performance.
What happens if attempt to keep search index on disk, rather than load it into memory...

## Slide 15: Testing Framework (BITS)
VisualVM: CPU and Memory monitoring
Python scripts for:
Setting up and taking down of application and data
Visualizing results with Matplotlib
Orchestrating tests & gathering data from tools
Makes use of common performance monitoring tools
Load generators: Iago, Jmeter.
CPU & Memory: VisualVM, Sematext SPM
Network: bwm-ng (coarse monitoring)
IO: iotop, dstat
Ganglia

## Slide 16: Future Work
Benchmarks / Workloads:
  A number of genomics and batch workloads are running on EC2, need to run on Firebox-0
  Currently no benchmark at the “WSC Executive” layer
  What other workloads to look at?
Aerospike vs Cassandra results:
  Understand Aerospike advantage on the D and E workloads (YCSB)
BITS:
  Effort just getting started
  There are other benchmarks / frameworks we can leverage

## Slide 17
Interactive Applications on Firebox-0
“WSC Executive” (Xen + resource partitioning)
Bulk Memory API (RAMCloud + transactions)
Interactive Applications
Cluster Manager (Mesos + interactive)
New component
Modified existing component
Network (Ethernet + Infiniband)
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about

## Slide 18
Batch Node
Batch Node
Interactive Node
10GBit Ethernet
Hypervisor (Xen)
Linux + Cluster Manager (Mesos)
Hadoop
Spark
App
App
Custom Services
Linux
#1 Multi-tenancy:
* Lack of isolation and QoS * Resource Accounting
#2 Interactive applications:
* Latencies (Tail-tolerance) * Elasticity * Failures
#3 Low Utilization (3-17% EC2 [1]):
* No sharing for interactive jobs * Redundant OS, language runtime, etc. data structures
Motivation: Warehouse Scale Computing
  Large, multi-tenant computers for the cloud
  Need dynamic resource allocations, resiliency to HW failure, power awareness

## Slide 19: Prior ParLab Work: Tessellation
Adaptive Resource Centric Computing (ARCC)
  Package applications into cells with explicit resource allocation and QoS guarantees
  Manage cells and resource allocation through a thin control plane
Service-oriented
  Cells subscribe to services provided by other cells
  Service subscriptions == resource allocations
Application1
QoS-aware
Scheduler
GUI
Service
Running System
(Data Plane)
Performance
Reports
Resource
Assignments
Control
Plane
Cell
Application1
Cell
QoS-aware
Scheduler
Block
Service
QoS-aware
Scheduler
NW
Service
Channels

## Slide 20: XARCC (aka Tessellation 2.0)
Observation: If the Tessellation kernel looks like a hypervisor, why not just use a hypervisor?
Tessellation implements these concepts on top of Xen
  Xen Domains become Cells
  Pluggable Schedulers allow us to implement custom scheduling policies
  Build network or other services in stub-domains (Xen domains intended to run drivers)
  Run Linux or a custom Library OS in the cells instead of mandating a particular interface

## Slide 21: XARCC
Physical Node
Tessellation OS (modified Xen)
Cell Scheduler
RAB
Service
Resource Monitor
Traditional Cell
Linux
Cluster Manager
Exec Framework
User App
Tess Cell
LibOS
User App
Unified Inter-node
and Intra-node IPC
interfaces
Most cells run modified
OS and applications to take
full advantage of Tessellation
features
Traditional virtual-machine
approaches continue to work
Tess kernel
Provides QoS and ARCC mechanisms
Resource allocation broker provides QoS and ARCC policy
Cell Communication Channels

## Slide 22: XARCC Scheduling: Status and Experiences
Status: Implemented gang scheduler on Xen
  Target performance predictability and synchronization overheads
  Benchmarked with Micro-benchmark and HPC-oriented solid deformation simulation
Experiences
  Micro-benchmark shows reduced variability when gang scheduling
  Macro-benchmarks suffer from reduced CPU utilization
  Takeaway: Tradeoff between utilization and predictability
Physical Node
Tessellation OS (modified Xen)
RAB
Service
Resource Monitor
Traditional Cell
Linux
Cluster Manager
Exec Framework
User App
Tess Cell
LibOS
User App
Cell Communication Channels
Cell Scheduler

## Slide 23: XARCC Library OS: Status and Experiences
Status: Implemented stripped down OS for cells (CellOS)
  Based on Guk1 and newLib2
  Supports a subset of POSIX
  Ported Pthread based benchmarks
Experiences
  Some single-application benchmarks are slower on CellOS than on Linux
  Debugging is very difficult
  Need to understand pros/cons better
Physical Node
Tessellation OS (modified Xen)
Cell Scheduler
RAB
Service
Resource Monitor
Traditional Cell
Linux
Cluster Manager
Exec Framework
User App
Tess Cell
LibOS
User App
Cell Communication Channels

## Slide 24: Future Work
Still early days: Most features yet to be implemented
  Resource Monitor
  Dynamic Allocation Policies
  Communication channels and service discovery
Run on FireBox-0 with BITS
  Can current workloads take advantage?
  Would custom HW change things?
Big area of interest: 2-level scheduling and resource allocation
  Gang scheduling needs deeper analysis and more sophisticated implementation
  Advantages of minimal OS vs Linux

## Slide 25: Questions & Feedback
This work is in the early stages
Where would you like to see this go?
  BITS
  XARCC
  FireBox-0

## Slide 26: Backup Slides

## Slide 27: Gang Scheduling Experiments
Micro-benchmark
  Run identical, compute-bound tasks on multiple threads repeatedly
  Record each time a thread completes its task more than a full iteration behind the others (a missed deadline)
Macro-Benchmarks
  HPC benchmark that models solid deformation in extreme environments
  Ran multiple instances of the benchmark
    Batch: Each instance ran one after the other
    Credit: Simultaneous execution on Xen’s default (non-gang) scheduler
    Gang: Simultaneous execution with gang scheduling

## Slide 28: Micro Benchmark Results

## Slide 29: Macro Benchmark Results

## Slide 30
Firebox Network
Without VMA* | 4.8 us
With VMA | 1.3 us
SockPerf Ping Pong Latency in Fbox
Firebox v0 | 1.7 us
RAMCloud HW [1] | 3.1 us
RDMA Ping Pong Latency
*VMA = Mellanox socket library with kernel bypass
Notes: Raw benchmark of Firebox Network
TODO:

## Slide 31
Aerospike/Cassandra Write Latency
Notes: Raw benchmark of Firebox Network
TODO: